## Slide 1
Students(Group M5)
Yuecan Fan, Sining Liu,
Weining Zou, Xi Zhang, Mengfei Zhang
Advisor
Professor Masoud Salehi
Senior CAPSTONE
Wireless Parking Detection System

## Slide 2
CONTENTS
01
Introduction & Background
Information
Hardware Design
Conclusion
02
03
04
05
Software Design
Video Exhibition

## Slide 3
Always have trouble in finding an available Parking position
Spend a high amount parking fee in a garage
Spend a lots of time to wait or hang around
。
Visualize real-time street parking data on App & Let user Self-Report
Parking Problem:
WHAT IS THIS TALK ABOUT
WHAT WE WANT
Use Sensors to detect the available parking spot on the Street
Wireless upload parking data to Cloud Server

## Slide 4
INTRODUCTION
Implementation has two parts:
• Hardware Design (Sensor Detection System& Wireless Upload Data):
• Use Magnetic Sensor to detect car movement
• Use Arduino board to build circuits and print out data
• Use XBee, XBee gateway to upload data to the cloud
• Software Design (Data visualization on the Map & App Basic functions)
• Registration and Sign In System
• Get Real-Time Data & User Self Report

## Slide 5
CONTENTS
Hardware Design
02

## Slide 6
Magnetic sensor
Arduino Uno
XBee
Logic level converter
Battery
Sensor Node

## Slide 7
Magnetic Sensor
Hmc5883l
Usually Use to make compass
Can detect magnetic field change in three directions

## Slide 8
Microcontroller
Arduino Uno
Most common microcontroller and easy to use
Can easily connect to HMC5883L and XBee
Modify the code to detect the change of z axis magnetic field that shows “1” for occupied and “0” for available

## Slide 9
Battery
Input Voltage for Arduino Uno is 7-12V
Duracell 9V battery

## Slide 10
Logic level converter and XBee
XBee’s operating voltage is 3.3V
Arduino Uno communicate at 5v. Even if we use the 3.3v pin, the serial, digital pins, everything, are all still operating at 5v.
So we need to connect logic level converter to protect XBee form burning out.

## Slide 11
Local Data Transfer

## Slide 12
Online Data Transfer
Digi Device Cloud

## Slide 14
Online Data

## Slide 15
CONTENTS
Software Design
03

## Slide 16
Coding on Hardware, Connection building & Storing
Program code on the ARUINO board to let Sensor print out two different status
Write Python to build the connection with gateway, differentiate each XBee and upload the data with small delay
Store User information
Write Swift Code to synchronously get real-time data

## Slide 17
Map View
The nearby available street parking information will show on the map.
User Self Report
Consider App may not include all parking information, this function design to let User Self Report.
User Registration
User can register using their email address. They will get an email confirmation from our server.
The app will provide user available parking slots.
App Functions

## Slide 18
Registration, Sign In System
Registration
Sign In

## Slide 19
Map View

## Slide 20
Programming
Use Swift to build functions and Story Board in Xcode to simulate the app, use PHP file to connect app with online database
Build-in Map
Use Google Map API to get user current location, and make real-time data showing
User Interface Design
Design icon and pictures in Photoshop, change default background and adjust the button location
The app use Xcode to build and
support iOS devices only at this time.
Implement the App

## Slide 21
CONTENTS
Video Exhibition
04

## Slide 22
CONTENTS
Conclusion
05

## Slide 23
Conclusion
New Solution to Park Problem
Collect real-time data
Save time and money
。

## Slide 24
Flaws and solutions
04
03
02
01
Sensor Network Design
Battery
Easier Registration System
Garage Information collected
As the number of devices increases, the Network Construction become more complicated.
Battery can only last for several days due to the XBee energy consumption.
Registration may require user fill too much Information
Garage parking information did not contain in our app

## Slide 25
Sensor Network Design
More XBee coordinators and Gateway added
Battery
Add Sleep mode to XBee.
Easier Registration System
Add Google account and Facebook account registration function
Garage Information
Collaborate with other Boston Parking website to get garage parking information
Solutions

## Slide 26
THANKS
Questions? Comments?